Investigation/Task List   1.2  12/15/04 DPC Prioritized

# Daytime Tasks

- Detector

  - Basic Verifications

    - All quads working properly

    - All quads working similarly (similar bias levels, well depth)

    - Measure saturation levels (well depth)

    - Measure conversion gain

    - Bad pixel map, count

    - Dark current

    - Read Noise

  - Redo Bias Dependence (sweep from Vbias = 0 to -1.2 V)

    - Dark current

    - Well depth

    - Read noise

  - Redo Detector Temperature Dependence (sweep from 25 to 40 K)

    - Dark current

    - Well depth

    - Read noise

  - Select best operating bias and temperature

    - Dark current

    - Well depth

    - Read noise

    - Conversion gain

- Readout Tests

  - Measure degree of ghosting

    - Or limits thereto

    - Evaluate mean ghosting for coadded images vs individuals

      - Is there a random component? (as per scope images)

  - Determine the fastest readout rate that is ghost-free

  - Determine relationship between read rate and conversion gain

  - Determine relationship between read rate and read noise

- Detector Temperature Stability vs Zenith Angle

  - Note detector temperature as function of Zenith Angle

  - Compare to experience with Hydrogen rain pipe

- Camera Block Tests

  - Basic motion testing

    - Moves to f/5, f/17, PV locations

    - Test for range of telescope declinations over which camera block moves properly

    - Test for range of telescope hour angles for camera block motion

    - Test camera block location repeatability

    - Determine best f/5, f/17, PV camera locations relative to nearest zero phase signal

- Pupil Viewer

  - Obtain high quality images of pupil

    - In K-band

    - In L-band

  - Step camera block to locate best PV position, examine effects of offsets

- Collimation Tests

  - determine location of optical axis on detector

    - minimum coma?

    - Intersection of coma axes across detector?

  - Adjust Mimir mounting to autoguider (with shims) to see if optical axis can be moved on detector

  - Where does ZEMAX place the optical axis on the detector?

    - What are the effects of tilted filters and the collimator L2 lens tilt?

- Readout tests, Part II

  - Exercise sub-frame readout

    - Range of selected image sizes

    - Range of image repeat rates, numbers

    - Test that array offsets are correctly logged to headers (so FFs may be used)

    - Measure dwell, dead, cycle times

  - Exercise Fowler Sampling

    - Test for expected reduction in read noise

    - Measure time penalties for data collection

  - Exercise Sample-Up-the-Ramp (SUR)

# Nighttime High Priority Tasks

- Focus Tests

  - Determine best f/5 focus for each of J, H, K, L bands

  - Determine best f/17 focus for same

  - Measure focus shift across field

    - Differential focus at corners versus center

    - PSF size, elongation as function of FOV location

  - Focus vs camera block position

    - Is coma a good tracer of camera position?

  - Determine best camera positions for f/5, f/17, PV cameras

- Detector Focus, Tilts

  - f/5 camera in, out of focus

    - compare to ZEMAX model

    - determine detector focus offset from current position

    - determine detector tilt, pitch

  - repeat 1. for f/17 camera

- Astrometry

  - Move star cluster across f/5 FOV

    - J, H, K, L bands

    - J + J-Corr

  - Same for f/17 FOV

    - J, H, K, L, M

    - No J-Corr

- Photometric & Polarimetric Tests

  - Photometric tests

    - Consecutive (short) images of a star field with range of delay times or integration times

      - Do the star brightnesses scatter photometrically as per their photon numbers, or is there extra noise?

  - Repeat the photometry test, but with HWP rotation

    - Range of integration times, cadences

  - Repeat 2., but with U, Q chopping instead of full HWP rotation

    - U chopping is 0 deg, 90 deg, 0 deg, 90 deg, etc

  - Observe polarized and unpolarized standards, moving each around in the FOV

    - Center

    - Corners

    - Mid-way to corners

  - Repeat 4., but for f/17 camera

  - Observe a suite of polarimetric standards and unpolarized standards

    - With f/5

    - With f/17

- Spectrometer Stability Tests

  - f/5 + narrowest slit

    - image sky lines to east

    - image sky lines to west

    - difference

  - Repeat 1. for f/17

  - Test repeatability of recovering slit position

    - Do imaging, spectroscopy pairs on SFR target (bright emission lines)

    - Repeat a. several times

    - Measure sky lines shift in those data

    - Measure target lines shift in those data

- Camera block focus stability

(f/5 only, f/17 presumed to have large depth of focus)

  - Focus in imaging mode at zenith

  - Refocus at Z-30 deg

  - Refocus at Z-45 deg

  - Refocus at Z-60 deg

  - Refocus at Z-75 deg

  - For each, wait for primary mirror support to catch up to elevation change

- Spectropolarimetric Tests

Goal is to determine polarimetric efficiency vs wavelength across the H-band – did I design the H-HWP incorrectly? Lab efficiency is about 72%, but should have been >95%.

  - For unpolarized standard star

    - H-HWP, H-band, WG, JHK grism with wide-ish slit

    - Collect polarimetric data with HWP rotation through a couple of full cycles

    - Move star on slit, repeat polarimetry

    - Repeat c. a few times

    - Redo all for U, Q chopping

  - Repeat 1. for one or two polarized standard stars

- J-Band Corrector

  - Does it have any effect? – Does putting it in and out of the beam change image quality?

  - Determine proper focus for the condition of the Corrector being in the beam

  - Measure PSF size, ellipticity across FOV

    - With J-Corr

    - Without J-Corr

  - Repeat astrometric star cluster multiple placements across the FOV to determine astrometric conversions

  - Come to a recommendation whether to use for wide field imaging or not

# Nighttime Lower Priority Tasks

- Spectroscopy Tests

  - f/17 tests

    - determine spectroscopy focus – focus by minimizing slit image size

    - compare to ZEMAX model

    - determine range of wavelengths obtained, and resolution

      - for JHK grism

      - for LM grism

      - for SED grism

    - What are the options for use of bandpass filters versus long pass filters?

      - Model with ZEMAX ahead of time

  - f/5 tests

    - determine optimal focus – narrowest slit, minimize image of slit

    - obtain deeper JHK flats to calibrate J-band better

    - observe spectroscopic standards on IRTF list

    - measure count rates versus wavelength to support exposure time estimator

- f/17 Shift-and-Add Speckle

  - Locate bright, close double with separation of 1 – 1.5”

  - Collect many short exposures (~100 – 200 each)

    - In J, H, K, L, M

  - Evaluate each image

    - Select those with smaller PSFs

    - Locate brightest star

  - Register, coadd

  - Measure FHWM, separation, Airy rings

  - Estimate Strehl ratio vs wavelength

- Extinction, Filter Transformations

I’m unsure of whether to do this at only f/5, only at f/17, or at both. M is unlikely to work at f/5, but there may be a color shift between the cameras due to the camera lens differences. Maybe best to do JHKL at f/5, then KLM at f/17 so there is some overlap. Needs some discussion

  - Measure photometric standards (IRTF list) at several airmasses

    - J, H, K, L, M

    - Determine extinction vs wavelength

    - Measure zenith sky background levels vs wavelength

    - Determine photometric offset magnitudes

    - Determine limiting magnitudes

    - Estimate system efficiency, throughput vs wavelength

  - Compute filter transformation coefficients

    - Against 2MASS

    - Against Bessel and Brett

- Slit Tests & SED Spectroscopy

  - Spectroscopy vs slit width

    - Resolution

    - Throughput (vs seeing) – what recommendations should we make?

  - “Eared Slit” tests

    - useful low-R spectroscopy?

  - SED spectroscopy – how can it be employed and calibrated?

    - 1.17LP + PK50

    - 1.85 LP

    - 2.8 LP

    - Z-machine use? Test on quasars

- Narrow-Band Imaging (H2-On, H2-Off)

  - Image a large star formation region (Orion?)

    - H2-On

    - H2-Off

  - Repeat 1., but move the SFR across the FOV to test for filter walk-off

  - Do same for f/17

  - Compute magnitude offset of On-Off (relative bandwidths)

- Fast Polarimetry (& Occultation) Mode Test

  - Exercise “streaming” photometric data collection over subframe into 3D FITS cube

  - Repeat 1. with HWP rotation also taking place

  - Repeat 2. with HWP in U, Q chopping mode

  - How fast can streaming take place? What are the subframe field sizes allowed versus cadence?

- Orion Star Forming Region as Demonstration of all Mimir modes

  - Direct Imaging

    - Wide-Field (f/5) Mosaics with dithering

      - L-band –if possible

      - K-band

      - J-band (with or without J-Corr?)

      - M-band – f/5 ???

      - H-band

    - Narrow-Field (f/17) Mosaics of core region

      - J

      - H

      - K

      - L

      - M

  - Speckle Imaging (f/17)

    - L-band

    - J-band

    - Both toward IRS2, BN/KL

  - Narrow-Band Imaging

    - H2-on, H2-off over large, overlapping field

  - Polarimetry

    - H-band + f/5 over wide field

    - H-band + f/17 over narrow field

    - Spectropolarimetry (H + f/5) toward IRS2, BN/KL

  - Spectroscopy

    - f/5

      - JHK toward core

      - LM too

      - SED ??

    - f/17

      - JHK

      - LM

      - SED ???

  - Polyproplyds

    - Deep f/17 imaging

    - Deep spectroscopy