## Slide 1
RIPS: the Rapid Imaging Planetary Spectrograph
First light at the Perkins 1.8m, 15 March 2018

## Slide 2
Overview
RIPS was designed for concurrent imaging and long-slit high resolution spectroscopy on the same detector
By utilizing “lucky imaging” techniques (i.e., via rapid imaging), RIPS can overcome atmospheric seeing, thereby precisely identifying the locations of spectral emissions around resolved Solar System objects
In addition, the natural motion of the slit across the target object allows for high resolution spectral imaging
RIPS has slots for 1” filter wheels or 2” single filters (in both imaging and spectral paths). Current available filters include:
  1”: NaI (45Å wide), SII (45Å), KI (45Å), various neutral density filter combinations
  2”: NaI (4Å), NaI (18Å), KI (14Å), OI (~20Å)
RIPS is controlled by 5 motors:
  Slit motor (~15 mm minimum width)
  Grating motor (echelle grating angle)
  Spectral focus motor
  Imaging (slit) focus motor
  RIPS rotation within cage (optional, rotates slit on sky)

## Slide 3
Schematic
38.6 L/mm echelle
slit
EMCCD
900 mm f.l. F/9 achromat
Light from telescope
white light
light from grating
light from slit
Re-imaging optics
1” filter wheel or 2” single filters
Plate for attachment to telescope
Rotation “cage”
R ~ 80,000 (for 3 pixel FWHM)
24.6 mÅ/pixel dispersion
(or 1.25 km/s/pixel at 5900Å)
Detector Andor iXon 1024x1024 EMCCD
Plate scale: 0.106″/pixel (on Perkins at f/17.5)

## Slide 4
RIPS: First light at Perkins 1.8m in AZ

## Slide 5
RIPS: First light at Perkins 1.8m in AZ
1” order sorting filter:
- NaI (45Å)
2” filter:
- NaI (4Å) + ND1
spectral channel
Imaging channel
30Å FSR
Mercury
(~96o phase angle)
spectral slit
solar Na D lines
(dark bands: 5890Å and 5896Å)
Mercury’s Na D lines (in emission)
20 fps (0.05 s integrations)
Notes: We have ~20 min of similar data, roughly half in K and half in Na